D
Diri_z_bottom = 15
No Neumann
With neumann

---
With neumann
IMS

---
Without Neumann

---
D_LED = 3.1e-5 m2/s
D_LF = 3.4e-7 m2/s
D_IMS = 1.2 e-5 m2/s
Dirichlet = 25 C at the bottom
Every other wall is Neumann du/dt = 0

---
Neumann = 0.1 C/s
Diri = 25 bottom

---
D_bottom = 25 C
Rest is neumann 0

---
Diri = 25C at the bottom
Neumann = 0

---
Neumann 0
Diri bottom = 25
50% of 16mA 2.5 V, ---> 20mW

---
Simple system
No Dirichlet BC, Neumann = 0
50% of 16 mA, 2.5V, Power 20 mW
Volume 500x500x100 um3

---
Heat source is divided by entire volume 500x500x100 um3
But heat is generated at the red plane

---
Simple system
No Dirichlet BC, Neumann = 0
50% of 16 mA, 2.5V, Power 20 mW
Volume 500x500x100 um3

---
Heat source turned off at 10e-3 second
No Dirichlet BC, Neumann = 0
50% of 16 mA, 2.5V, Power 20 mW
Volume 500x500x100 um3
Heat source turned off at 10e-3 second

---
Gold connector added
XZ-plane at y = 35

---
YZ Section
XZ Section
Neumann 1000
Diri 25

---
Neumann 0
Diri 25

---
Diri 25
Initial temp = 25
Neumann 0
Power 16mA*2.5V = 40 mW

---
Assuming that the whole LED is a heat source

---
For GaAs
BB r ~ T4-T04
Convection ~ T-T0
At 200 C
DT/dt = 0.1 C/ms
With convection
At 200 C
DT/dt = 0.01 C/ms
With BB radiation

---
Diri 25
Initial temp = 25
Neumann 0
Power 16mA*2.5V = 40 mW

---
Diri 25
Initial temp = 25
Neumann 0
10% of Input Power 16mA*2.5V = 40 mW = 4 mW

---
With blackbody radiation decay and newtons convection decay